## Slide 1: Test Bed for Industrial Wireless Communications: A Collaborative Robot Work-Cell Use Case
Yongkang Liu
2019-05-08

## Slide 2: Agenda
Goals and objectives
Test bed overview
Initial results

## Slide 3: Goals and Objectives
Build a measurement platform for evaluating wireless capabilities of supporting mission-critical industrial communications
  Collect data from production operations, machining tools, and networks
  Unveil interactions between operational technologies (OT) and information technologies (IT) in discrete manufacturing processes
  Test various network techniques to support low-latency, high reliable data transmissions
  Verify modeling methods and statistical patterns

## Slide 4: A Collaborative Robot Work-Cell
HMI
Robots
Supervisor
Queue
Machining tools

## Slide 5
Operator
Inspector
Work Station Array
A
B
C
D
Job Queue
Work-Cell Use Case – Robotic Machine Tending
Supervisor
CNC (Emulator)
Notes: Probing sensors are attached to the inspector to obtain the real inspection result
Overview of the operation procedures (physical part)
Operator: deliver
Inspect: inspection
Workstation (pedestal): processing

## Slide 6
CNC_1_main()
SCHDL_main()
SCHDL_Sub_CNC()
CNC_2_main()
CNC_3_main()
CNC_4_main()
UR_OPT_main()
Order_main()
Queue_main()
UR_INS_main()
SCHDL_Sub_INS()
arrCNC[1]
arrCNC[2]
arrCNC[3]
arrCNC[4]
gvQueue
gvUR1
gvUR2
gvOrder
SCHDL_Sub_Queue()
gvSch
ADS
HMI
VisuRules()
Supervisor
Interfaces
Variable Lists
Scheduler
Visualization
I/O
Modbus
Job-Based
Order-Based
gvSys
gvCNC
Notes: Supervisor code is maintained at the project’s GitLab repo:
https://gitlab.nist.gov/gitlab/el-wireless/el-iws-workcell/tree/plcFeature/PLC/TwinCAT_Emulator_Server

## Slide 7
Operator
Inspector
Work Station Array
A
B
C
D
Job Queue
Work-Cell Use Case – Robotic Machine Tending
Supervisor
CNC (Emulator)
Notes: Probing sensors are attached to the inspector to obtain the real inspection result
Overview of the operation procedures (physical part)
Operator: deliver
Inspect: inspection
Workstation (pedestal): processing

## Slide 8
gvDiag
gvSys
gvIoi
gvComm
gvSta
CNC Emulator
IOI_main_IN()
IOI_main_OUT()
STA_main()
COMM_main()
DIAG_main()
I/O
ADS
Variable Lists
Function Modules
Notes: CNC Emulator
In the architecture, functions are grouped by their roles: processing, communication, I/O, and diagnostics.
Emulator code is maintained at the project’s GitLab repo:
https://gitlab.nist.gov/gitlab/el-wireless/el-iws-workcell/tree/plcFeature/PLC/TwinCAT_Emulator_CNC

## Slide 9
Operator
Inspector
Work Station Array
A
B
C
D
Job Queue
Work-Cell Use Case – Robotic Machine Tending
Supervisor
CNC (Emulator)
Notes: Probing sensors are attached to the inspector to obtain the real inspection result
Overview of the operation procedures (physical part)
Operator: deliver
Inspect: inspection
Workstation (pedestal): processing

## Slide 10: UR3 System (1/2)
A UR3 system includes a control box, a 6 Degree-of-Freedom (DoF) robot, and UR3 peripherals which we refer to as robotic end effector devices (REEDs). In this testbed, each UR3 is equipped with a gripper and a 6-axis force torque (F/T) sensor. The F/T sensor is further divided into the sensing unit and a compute box.
REEDs
(Illustration only: Camera is not used in this test bed)
F/T compute box
UR Control box
UR robot

## Slide 11: UR3 System (2/2)
REEDs communicate with UR control box
Current F/T firmware only supports an error-free Ethernet connection with the control box
  Any disconnection issue leads to a system error which requires manual reset
Gripper
F/T sensor
F/T compute box
UR Control box
UR robot
External

## Slide 12: One OT Procedure (Job @ y)
RC
(Optr.)
RC
(Insptr.)
PLC
(Supvsr.)
PLC
(CNC x)
PLC
(CNC y)
StaRprt: Complete@x
StaRprt: Empty@y
IF Sys. Unlocked == TRUE THEN
SCHDL: Move x to y;
Sys. Locked;
StaRprt: Ready@UR2
Move route:
x -> y
New Job Info.
Part Arrival
Job Complete
StaRprt: Ready@UR1
Sys. Unlocked;
…
Inspect. Ready
Inspect. Req. @ y
IF Sys. Unlocked == TRUE THEN
SCHDL: Inspect @ y;
Sys. Locked;
Inspect @ y
Inspect Done @ y
StaRprt: Ready@UR2
Job Start
Inspect. Rsp
StaRprt: Complete@y
StaRprt: Ready@UR1
Sys. Unlocked
…
Robot_OUT
Notes: Key is gvSch.bMoveLocked for safety (at any moment, at most one job is moving between machines by one robot)
The inspection request has a higher priority at the scheduler and any inspection request should be queued in case the system is locked when the request arrives.

## Slide 13
Operator
Inspector
Work Station Array
RC
UR3
UR3
Robot Controller (RC)
PLC
Supervisor
Switch
Analysis device
(Server)
Robotic end effectors and sensors (REES)
Process data
Measurement data
Connectivity
Measurements
REES
PLCs
Network
Notes: Two parallel system layers: robot control system test use case and the measurement system
  Robot control system: robots, simulated work stations, and other work-cell devices, which are connected by wires or wirelessly going through Ethernet
  Measurement system: fully synchronized, capture system operation data as the reference for performance comparison

## Slide 14: Test Bed Measurements
Three sets of data
  Network traffic (WireShark)
    TCP/IP packets: ADS/AMS, Modbus, etc.
    Captured at switch’s mirroring port or at a network test access point (TAP/nTAP)
  Customized subscription of OT process status
    PLC (Supervisor)
    UR3 status: Real-time data exchange (RTDE)
OT-IT event alignment
  Accurate timing: IEEE 1588-2008 (PTPv2)
  PTP-synced timestamps being available for all data collection (PLC, RTDE, WireShark)

## Slide 15
UR3 (OPT)
Control box
CNC_1
CNC_2
CNC_3
CNC_4
OPT_F/T
Compute box
Supervisor
NTP Sync
Grandmaster (GM)
TSN Switch
Cisco IE-3000-8tc
Data Collector
LinuxPTP
UR3 RTDE
Wireshark
PLC
PTP Sync
PLC 1588 Term
INS_F/T
Compute box
UR3 (INS)
Control box
Main Switch (24 ports)
Netgear GS9724Tv4
Cisco IE-2000-8tc
Netgear GS108
Port mirroring
(Ingress & Egress)
Measurement Subnet
Production Subnet
Notes: Baseline network connections:
Production data (Green), measurement data (Red), and PTP synchronization (Purple)

## Slide 16: Dual TAP Measurements (Modbus)
PLC
(Supervisor)
Modbus Request (Read/Write)
Modbus Response
UR3
(Operator
/Inspector)
Network analyzer
Lab Network
TAP
TAP
Time
Application
Round-trip time (RTT)
One-way link delay
Link RTT
Process
-ing delay

## Slide 17: Statistical Results 1
One-way link transmission delay
  First 40 minutes in a 100-part production :
    Average end-to-end (SUP-OPT) delay: 65.94914005236618 us

## Slide 18: TAP Measurements (ADS/AMS)
PLC
(Supervisor)
ADS Request (Read/Write)
ADS Response
PLC
(CNC x)
Network analyzer
Lab Network
TAP
Time
Application
Round-trip time (RTT)
One-way link delay
Link RTT
Process
-ing delay

## Slide 19: A Trace File Example
10.10.0.5
Supervisor
10.10.0.8
CNC_3
#94
#99
#120
#121
#138
#139
#152
#160
#176
#180
#199
#204
CNC Status Update
(10 Hz)
STRUCT mStaRrpt
{
_nStaID: UINT; # 16b
_nState: UINT; # 16b
_nCode: UINT; # 16b
_bQueueOn: BOOL; # 8b
}
Pkt ID | State Flag | Invoke ID | ADS Data | Index Group | Index Offset
#94 | ADS Req. | 0xff7d000b | GET_SYMHANDLE_BYNAME | 0x0000F003 | 0x00000000
#99 | ADS Resp. | 0xff7d000b | No Error |  | 
#120 | ADS Req. | 0xff7d000c | RD/WR_SYMVAL_BYNAME | 0x0000F005 | 0x58800039
#121 | ADS Resp. | 0xff7d000c | No Error |  | 
#138 | ADS Req. | 0xff7d000d | RELEASE_SYMHANDLE | 0x0000F006 | 0x58800039
#139 | ADS Resp. | 0xff7d000d | No Error |  | 
Working zone
Safety alert
(10 Hz)
Pkt ID | State Flag | Invoke ID | ADS Data | Index Group | Index Offset
#152 | ADS Req. | 0xff650012 | GET_SYMHANDLE_BYNAME | 0x0000F003 | 0x00000000
#160 | ADS Resp. | 0xff650012 | No Error |  | 
#176 | ADS Req. | 0xff650013 | RD/WR_SYMVAL_BYNAME | 0x0000F005 | 0x340000a1
#180 | ADS Resp. | 0xff650013 | No Error |  | 
#199 | ADS Req. | 0xff650014 | RELEASE_SYMHANDLE | 0x0000F006 | 0x340000a1
#204 | ADS Resp. | 0xff650014 | No Error |  | 
Notes: https://infosys.beckhoff.com/english.php?content=../content/1033/tcadsdeviceplc/html/tcadsdeviceplc_indexadsservice.htm&id=

## Slide 20: RTT of CNC Requests
CNC_3 status updates
Supervisor response time included
First 40 min in a 100-part production
1 outlier

## Slide 21: Conclusion
Test bed and data will be released as reference model products for industrial wireless communication studies

## Slide 22: Backup Slides
PTP
Network topology

## Slide 23: PLC Measurement Interface
Main HMI view
HMI view for measurement configurations
FileOpenSave dialog box

## Slide 24: PLC Measurement Timing & PTP Sync
PTP: 10.10.0.121
NTP: 10.10.0.120
Grandmaster (GM)
Boundary Clock (BC)
Ordinary Clock (OC)
IEEE 1588-2008 (PTPv2)
End-to-end Delay Mechanism
IPv4 UDP multicast
EtherCAT distributed clock (DC)

## Slide 25
10.10.0.5
10.20.0.25
10.20.0.26
10.10.0.6
10.10.0.8
10.10.0.9
10.10.0.7
OPT
Control box
CNC_1
CNC_2
CNC_3
CNC_4
OPT_FT
Compute box
10.20.0.15
10.20.0.16
Supervisor
Grandmaster (GM)
TSN Switch
Cisco IE-3000-8tc
RIVA
10.10.0.91
LinuxPTP
UR3 RTDE
Wireshark
PLC
PTP: 10.10.0.121
10.10.0.93
10.10.0.92
10.10.0.51
PLC 1588 Term
INS_FT
Compute box
INS
Control box
Kontron Switch
Port mirroring
(Ingress & Egress)
Suggested Baseline TSN Topology
(Option 1b: 2 UR Subnets)
Kontron Switch
Kontron Switch
Notes: Baseline network connections:
Production data (Green), measurement data (Red), and PTP/TSN links (Purple)

## Slide 26
10.10.0.5
10.20.0.25
10.20.0.26
10.10.0.6
10.10.0.8
10.10.0.9
10.10.0.7
OPT
Control box
CNC_1
CNC_2
CNC_3
CNC_4
OPT_FT
Compute box
10.20.0.15
10.20.0.16
Supervisor
Grandmaster (GM)
TSN Switch
Cisco IE-3000-8tc
RIVA
10.10.0.91
LinuxPTP
UR3 RTDE
Wireshark
PLC
PTP: 10.10.0.121
10.10.0.93
10.10.0.92
10.10.0.51
PLC 1588 Term
INS_FT
Compute box
INS
Control box
Kontron Switch
Port mirroring
(Ingress & Egress)
Suggested Baseline TSN Topology
(Option 2: 1 UR Subnet)
Kontron Switch
Notes: Baseline network connections:
Production data (Green), measurement data (Red), and PTP synchronization (Purple)

## Slide 27
10.10.0.5
10.20.0.25
10.20.0.26
10.10.0.6
10.10.0.8
10.10.0.9
10.10.0.7
OPT
Control box
CNC_1
CNC_2
CNC_3
CNC_4
OPT_FT
Compute box
10.20.0.15
10.20.0.16
Supervisor
Grandmaster (GM)
TSN Switch
Cisco IE-3000-8tc
RIVA
10.10.0.91
LinuxPTP
UR3 RTDE
Wireshark
PLC
PTP: 10.10.0.121
10.10.0.93
10.10.0.92
10.10.0.51
PLC 1588 Term
INS_FT
Compute box
INS
Control box
Kontron Switch
TBD: Wireless TSN Topology
(1 UR Subnet Case)
Which NUC will act as the WLAN AP? (The AP may needs to connect to the IE-3000 for PTP referent time.)
TAP
Notes: Baseline network connections:
Production data (Green), measurement data (Red), and PTP synchronization (Purple)