## Slide 1: Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Richard Candell
PhD Thesis
29 September 2020

## Slide 2: About Me
Richard Candell has over twenty years of experience in telecommunications system engineering with extensive experience in the design and evaluation of wireless communications systems. Mr. Candell spent twelve years developing, testing, and deploying secure wireless technologies for commercial and defense applications. He served as the lead systems engineer in developing spread spectrum interference cancellation and performance evaluation strategies for satellite ground stations and mobile phased array beam steering transceivers. He holds patents in successive interference cancellation and transmission burst detection applied to spread-spectrum satellite communications signals. Mr. Candell holds a BS and MS degree in Electrical Engineering from The University of Memphis. He joined the NIST in 2014. His current research interests include the performance impacts of wireless networks on industrial sensing and actuated control applications for mobile robotic, manufacturing, and safety applications. Mr. Candell was the primary contributing author of the Guide to Industrial Wireless Systems Deployments (NIST AMS 300-4) and the chair of the NIST Industrial Wireless System technical working group.

## Slide 3: The NIST Industrial Wireless Project
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Thesis Presentation 29 September 2020
Richard Candell

## Slide 4: Historical Approach to Research/Guidance
Field Data
Models
Interference Models
Propagation Models
Experiments
Testbed
Guidelines
Brown field control
Channel Models
Increase data
More Reliable
Live Factories
Improve Safety
Precision Measurements
Meetings
Conferences
Manufacturing Models
Simulations
Best Practices
Spur Innovation
Spectrum Sensing
Advanced control solutions
Notes: It doesn’t make sense to deliver guidelines without considering the factory performance under different scenarios.
MY APPROACH: Combine my research at NIST with PhD research

## Slide 5: Collaborators: Past and Present
Notes: Contacts:
All collaborators share a common interest in industrial wireless. They will all participate and respond to our guidelines document.
Honeywell – Phillip Ng (new contact, very interested in outcomes)
Boeing - Al Salour, Bala Chidambaram, Mark Vanhorne ()
Ford - Mike Read, Eric Newman
Chevron – Brent Aube, Stacie Smith, Greg Laframboise (retired)
Phoenix Contact – Justin Shade, Lee Boice
Honeywell: Phillip Ng (new contact)
Yokagawa – Toshi Hasegawa
WSSC – Jacob Brodsky, review of our guidelines
PiControl Solutions – Steve Howes (control design solutions for wireless)
IEEE – Various, Victor Huang (IMS), Kim Mann (IES), Pat Kinney (IEEE/DETNET)
ISA – Jay Werb, Sterling Rooke, Herman Storey
UMD – Shuvra Bhattacharya
Michigan – Wayne Stark
Delware - Chien-Chung Shen
Ultra-3eTI – John Fosssaceca (he left for ARL)

## Slide 6: Technical Working Group Established
IEEE Sensors Applications Symposium
Established March 13, 2017
Key Participants at the time
  Boeing
  ABB
  IEEE
  ISA
  NIST

## Slide 7: Measurement Campaigns
Boulder Steam Plant
Auto Factory
Machine Shop

## Slide 8: Cart-based Measurements

## Slide 9: Current Project Objectives: Two Tracks
Track 1: Provide Guidance to Industry Deliver comprehensive, measurement science-based guidelines in the selection, deployment, and optimization of the wireless technologies in specific manufacturing environments.
Track 2: Address Emerging Needs Conduct research that advances the state of technology of wireless-based automation systems in which time, reliability, energy, and scale are joint considerations.

## Slide 10: Addressing Emerging Needs
Reliability Studies
Testbed Activities
Measurements in real industrial settings
Machine Learning for replications
Time Sensitive Networking Studies
Special CPS Considerations
Real Uses Cases
CPS Performance Analysis
Millimeter-Wave Propagation Studies

## Slide 11: The NIST Industrial Wireless Testbed
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Thesis Presentation 29 September 2020
Richard Candell

## Slide 12: NIST Industrial Wireless Testbed
Discrete/Fast Processes
e.g. Mechanical Assembly
Slow Processes
e.g. “TESIM” Chemical Reactor
Process
Control
Discrete
Manufacturing
Past Focus
Current Focus

## Slide 13: Key Capability: RF Channel Emulator
Transmission Delay
Path loss
Multipath
Fading
Interference
Mobility Radios
Mobile Surroundings
Recreates the Factory’s Radio Environment in the Lab

## Slide 14: Past Testbed Incarnations
1 - NIST - Tennessee Eastman chemical plant simulator
2 - NIST - 3D gantry system
3 - NIST - Force seeking apparatus
4 - NIST - Dual-robot machine tending with inspection
5 - Intel Dual-robot tether apparatus using TSN
(1)
(2)
(3)
(4)
(5)

## Slide 15: IWS Demonstration Platform
RF Channel Emulator
Dual Cobots
RF
Shielding
IEEE 1588 Master
Supervisor
CNC Sims
TSN Capable

## Slide 16: Example: Chemical Reactor Control
Sensors
Level
Temperature
Pressure
Flow
Composition
Position
Actuators
Valve position
ON/OFF
Set-points
Reconfigure
Thresholds
Path Loss
Delays
Multipath
Interference
Controller

## Slide 17: Thesis
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Thesis Presentation 29 September 2020
Richard Candell

## Slide 18: Thesis Motivation
Discover practical test and evaluation methods for assessing performance of an industrial workcell thereby improving security, safety, and reliability.

## Slide 19: Research Objectives
Exploration of Requirements: Industrial applications vary widely depending on the needs of the application. Applications may range from Condition Monitoring (CM) in which the required reliability and tolerable latency is high to applications such as hard real-time applications for safety integrated systems (SIS) in which reliability and latency are strictly controlled. Much of the information regarding communications requirements of these widely varying applications are based on opinion with little validation specified. Moreover, the information found can be confused by media hype and speculation. Therefore, a very important and first step in the research was to explore the requirements as stated by reputable sources such as international standards organizations and peer-reviewed papers and provide a distilled, realistic perspective uncluttered by hype and supported by experimental data or analysis of the underlying use cases.
Architectural Decomposition: The next important element within the research was to understand the composition of a factory workcell to include its constituent parts and interfaces. The goal in doing so was to discover and model the important CPS elements of a factory workcell and how those elements connect, interrelate, and conduct information in a general sense. Therefore, our objective was to create a reusable exploratory model of the CPS that is a factory workcell in which wireless communication is the primary mode of communication.
Discovery by Prototyping: During the discover process of the research work, we aimed to perform our research using real-world data from physical experiments. Since the required resources were available and at our disposal, our research objective was to conduct as much of the research using actual devices such as industrial automation and communication equipment as possible.
Non-traditional Analysis: Our final goal was to explore through experimentation the use of new data organization methods and learning approaches to analyze data taken from laboratory experiments. Therefore, our research objective was to apply database technology and machine learning algorithms in ways that had not yet been adopted or used for analysis of CPS performance analysis.

## Slide 20: Contributions
Requirements [1]–[4] An examination of the wireless technology landscape is conducted. Existing and future wireless technologies are assessed for their appropriate applicability to industrial use cases.
Modeling [5], [6] In an effort to better understand the architectural composition of the workcell using industrial wireless communication, modeling techniques are used to identify and decomposed the parts, interfaces, and data flows. SysML is adopted for this process and a proposed modeling library is created and presented. The model with conceptual diagram is made publicly available independent of the tool that was used to create the model.
Application of Graph Databases [7], [8] A method is developed for collecting, cleaning, organizing, and presenting the cyberphysical performance indicators of experiments run within the NIST Industrial Wireless Testbed. The method developed utilizes the Neo4j graph database and is presented as a novel approach as compared to traditional approaches using relational database, spreadsheets, and raw file processing.
Machine Learning [9], [10] A machine learning technique is developed and applied to the prediction of signal-to-interference levels within a wireless factory workcell network employing a robot arm within a force-seeking apparatus. The machine learning method allows a trained network to accurately determine the signal-to-interference level using the physical state of the robot arm rather than the state of the wireless link itself.

## Slide 21: Publication List
[1] R. Candell and M. Kashef, “Industrial wireless: Problem space, success considerations, technologies, and future direction,” in 2017 Resilience Week (RWS), Sep. 2017, pp. 133–139, doi: 10.1109/RWEEK.2017.8088661.
[2] K. Montgomery, R. Candell, Y. Liu, and M. Hany, “Wireless User Requirements for the Factory Work-cell,” 2019. doi: https://doi.org/10.6028/NIST.AMS.300-8.
[3] R. Candell, M. Kashef, Y. Liu, K. B. Lee, and S. Foufou, “Industrial Wireless Systems Guidelines: Practical Considerations and Deployment Life Cycle,” IEEE Ind. Electron. Mag., vol. 12, no. 4, pp. 6–17, 2018.
[4] R. Candell, M. Hany, K. B. Lee, Y. Liu, J. Quimby, and K. Remley, “Guide to industrial wireless systems deployments,” Gaithersburg, MD, Apr. 2018. doi: 10.6028/NIST.AMS.300-4.
[5] R. Candell, M. Kashef, Y. Liu, and S. Foufou, “A SysML representation of the wireless factory work cell,” Int. J. Adv. Manuf. Technol., vol. 104, no. 1–4, pp. 119–140, Sep. 2019, doi: 10.1007/s00170-019-03629-x.
[6] R. Candell, “A Model of a Wireless Factory Work-Cell Using the Systems Modeling Language,” J. Res. Natl. Inst. Stand. Technol., vol. 123, p. 123018, Oct. 2018, doi: 10.6028/jres.123.018.

## Slide 22: Publication List (2)
[7] R. Candell, M. Kashef, Y. Liu, K. Montgomery, and S. Foufou, “A Graph Database Approach to Wireless IIoT Work-cell Performance Evaluation,” in Proceedings of the 2020 IEEE International Conference on Industrial Technology, Feb. 2020.
[8] M. Kashef, Y. Liu, K. Montgomery, and R. Candell, “Wireless Cyber-Physical Systems Performance Evaluation through a Graph Database Approach,” J. Comput. Inf. Sci. Eng., pp. 1–19, 2020, doi: 10.1115/1.4048205.
[9] R. Candell, K. Montgomery, M. Kashef, Y. Liu, and S. Foufou, “Wireless Interference Estimation Using Machine Learning in a Robotic Force-Seeking Scenario,” in 2019 IEEE 28th International Symposium on Industrial Electronics (ISIE), Jun. 2019, pp. 1334–1341, doi: 10.1109/ISIE.2019.8781418.
[10] R. Candell, K. Montgomery, M. Kashef, Y. Liu, and S. Foufou, “Machine Learning Based Wireless Interference Estimation in a Robotic Force-Seeking Application,” ISA Trans., 2020, doi: pending.
[11] R. Candell and S. Foufou, “Smart Manufacturing Testbed for the Advancement of Wireless Adoption in the Factory,” in Proceedings of the 17th International Conference on Product Lifecycle, 2020, [Online]. Available: https://www.plm-conference.org/.
[12] M. Kashef, R. Candell, and S. Foufou, “On the Impact of Wireless Communications on Controlling a Two-Dimensional Gantry System,” in ASME 2019 14th International Manufacturing Science and Engineering Conference, 2019, vol. Volume 1:, doi: 10.1115/MSEC2019-2896.

## Slide 23: Introduction to Smart Manufacturing and IIoT
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Thesis Presentation 29 September 2020
Richard Candell

## Slide 24: Model of a cyberphysical system

## Slide 25: CPS Necessities
The automation system must become state aware and adaptive to knowledge of the trends in electromagnetic spectrum occupancy and acute events;
Intelligence of the automation system must move closer to the physical system. This means moving the intelligence for control to the actuator; and
Performance test methods must be developed and incorporated into the industrial fringe devices. The test methods must be dependable and at the same time easy to use by factory personal not trained in the technicalities of wireless communication.
Existing Wireless communications protocols must be analyzed and adapted, and new protocols must be developed to balance reliability, latency, and scalability.
Security of the network must be maintained and must include availability as a paramount characteristic.

## Slide 26: Industrial Wireless Technologies
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Thesis Presentation 29 September 2020
Richard Candell

## Slide 27: Wireless Applicability to Industrial Systems
R. Candell and M. Kashef, Industrial wireless: Problem space, success considerations, technologies, and future direction, in 2017 Resilience Week (RWS), Sep. 2017, pp. 133139.

## Slide 28: Subsequent Requirements Work

## Slide 29: SysML: Workcell Architectural Decomposition and Analysis
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Thesis Presentation 29 September 2020
Richard Candell

## Slide 30: Conceptual Diagram
Device
  Wireless Device
  Controller
Controller
  Robot Controller
  PLC
Applications
IWN
Radio Channel
Service
Constraints

## Slide 31: Packages

## Slide 32: Robotics

## Slide 33: Constraints
Allows us to model mathematically or programmatically effects of behavior within a block.

## Slide 34: Radio Channel and Constraints

## Slide 35: Industrial Wireless Network (IWN)

## Slide 36: Service (of an IWN)

## Slide 37: Clock

## Slide 38: Spectrum Monitoring System (SMS)

## Slide 39: Example IBDs of Factory Workcells

## Slide 40: Application of the Graph Database to CPS Discovery
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Richard Candell

## Slide 41: Contribution of the GDB Approach
Primary contribution of this component of the thesis is to demonstrate the interconnection between the industrial (wireless) network and physical operations through the modeling and capture of the performance data, the data relationships, and the analysis of physical action performance when network performance is degraded. The use of the graph database makes that possible.

## Slide 44
Supervisor
Inspector
Non-PTP Switch
Operator
Non-PTP Switch
OPT_RC
OPT_FT
CNC_2
CNC_1
Two PTP capable switches
(22 ports combined)
CNC_3
CNC_4
TAP
TAP
TAP
TAP
TAP
TAP
TAP
Traffic Generator
Traffic Sink
AP
Eth->Wi-fi
Sniffer
NUC
PLC
Wi-Fi Router
Robot Controller(RC)
Force-Torque(FT) Sensor
Eth->Wi-fi
INS_FT
INS_RC

## Slide 47: Example Query Using Cipher
MATCH p=(a:Actor {
name:'Supervisor'
})--(t:Transaction)--(b:Actor) , p2=(m:Message)-->(t)
WHERE t.timeStart>T AND t.timeStop<T+1
RETURN p, p2

## Slide 48: Example Query Using Cipher
MATCH p=(a:Actor {
name:'Supervisor'
})-->(t:Transaction {
timeStart:Ts
})<--(b:Actor {
name:"CNC-1"
})
WITH p, a, b, t
MATCH p1=(a)-->(m:Message)<--(b), p2=(m)-->(t), p3=(a)-[:HAS]-(), p4=(a)<-[:COLOCATED_WITH]-()-[:PRODUCED]->(q:QoSReport), p5=(a)-[:CONNECTED_THROUGH]-(), p6=(b)-[:HAS]-(), p7=(b)-[:CONNECTED_THROUGH]-()
WHERE q.time>t.timeStart AND q.time<t.timeStop
RETURN p, p1, p2, p3, p4, p5, p6, p7

## Slide 49: Results from Query
Wired Performance Baseline
Wireless with 2-Stream Interference

## Slide 50: Machine Learning in a Robotic Force Seeking Application
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Thesis Presentation 29 September 2020
Richard Candell

## Slide 57: Initial Results Against Segment Size, M

## Slide 58: Subsequent Regressor Comparisons
Random Forest - definition

## Slide 59: Subsequent Comparisons

## Slide 60: Variance and MSE of Various Regressors

## Slide 61: Thoughts and Future Direction
Performance Estimation, Testing, and Control of Cyber-Physical Systems Employing Non-Ideal Communications Networks
Thesis Presentation 29 September 2020
Richard Candell